IoT Basics
With the ESP-(WROOM-)32
© 2023 Severin Mairinger

---
Development Environment
- Resources: https://github.com/sevsev9/iot-workshop-0123
- Arduino IDE
- Esp32 Board Scripts
  - Paste the URLs under File > Preferences

---
Development Environment
Download the “esp32” Board Scripts

---
SSD1306 & BMP280

---
In the Meantime - ESP32 Specs
- 2 x Xtensa 32bit LX6 Cores (80MHz – 240MHz)
- 448KB ROM, 520KB SRAM (Up to 11MB external)
- Realtime Clock with Low-Power Co-Processor
  - Pins with Power-On Interrupts
  - 8KB FAST & SLOW Memory
- WiFi & Bluetooth LE
- I2C, I2S, SPI, PWM, RMT, PCTN, UART, Ethernet MAC
- SDIO Host/Slave, TWAI (CAN) Controller
- 12x 12bit ADC, Touch, 2x 8bit DAC, Hall Sensor, 34x GPIO (all PWM)

---
SSD1306 – 0.96” OLED Display
- Resolution: WHOPPING 128x64
- Two Color Display (lines 0, 1 yellow, the rest blue)

---
BMP280 – Temperature and Pressure
- Operation Range:
  - Pressure: 300 … 1100hPa
  - Temperature: -40°C … 85°C
- Accuracy:
  - Pressure (Abs.): +- 1hPa @ 0.01 hPa
  - Temperature: +- 0.5°C @ 0.01 °C
- Power Consumption @ 1Hz: 3.4µA @ 1.2 – 3.6V input
- I²C and SPI Capable

---
I²C Protocol
- 2 Pins
  - SCL: Serial Clock
  - SDA: Serial Data
- Synchronous Protocol
- Speeds:
  - Standard Mode = 100 kbps
  - Fast Mode = 400 kbps
  - High Speed mode = 3.4 Mbps
  - Ultra Fast Mode = 5 Mbps
- # of Devices per Channel = 1008

---
I²C Protocol
- Start Condition: (SDA | H → L) → (SCL | H → L)
- Stop Condition: (SCL | L → H) → (SDA | L → H)
- 8 bit Data Frame
- Every Slave Receives every package
- Slave only reacts, if the address matches its own

---
Any Questions so far?

---
Wiring

---
Serial Communication

---
Let’s Print Something on the Display
The Screen Settings

---
I²C Display
Define the display globally

---
I²C Display

---
Moving to IDE